Overview

MP-3000(now is RK-3000) Series Vibration tester is a type of machine which can test the anti-vibration of some electronic machines and other products.

The appearance and technology of this Vibration tester is better than other vibrators’.

The machine uses advanced microcomputer control technology. It can remember the time the current shock. Not only will not loss of data be because out of power, but also can monitor the vibration amplitude.

It has another feature  is that when the machine has been shut down or when a sudden power off, the machine will automatically remember the current vibration time, and automatically reset to prevent the impaction of unstable voltage and burned by the machine when re-boot.

The vibrators be sold on the market today always have many shortcomings that led to their failure rate is very high. It will increase the maintenance costs.

The machine uses advanced microcomputer control technology. It can prevent and resolve the shortcomings above, so that the operating performance of our vibrator is more stable and reliable.

ⅠTechnical parameters

- The Max load：40kg.

- Power input：AC220v/50Hz（±2%）.

- Monitor displays the value of vibration amplitude：100%（Display：100）.

- Time setting：1second -100 hours（Display：99：59：99）。

- Power：0．9kw。

- Vibration direction: vertical.

- Adjustable amplitude without load：0-2mm

A：load with 0-15kg：0-2mm

B：load with 30-40kg：0-1．8 mm

- Table Size：400 mm×350 mm×16 mm（L×W×H）.

ⅡOperation（Panel）

①：POWER Switch  ②：Display of the Vibration amplitude  ③：Display of vibration time ④：Indicator when  running ⑤：Indicator when stopping      ⑥：RUN/STOP Button ⑦：SET button  ⑧：Amplitudes decrease button/ RESET /VOLUME（—） ⑨：Amplitudes increase button/VOLUME（+）

  - First take off the fixed crews on the table, then fix the machine on the strong ground which is level, or the strong table which is level. It needs no other special facilities, but you must ensure that the machine is fixed and the table is level.

  - The products being tested must be fixed by some clamp or some fixed rope on the working table .Please let the center of the products placed at the focus as possible.

  - Please make sure the voltage input is AC220V. In order to ensure the accuracy of the measured results, please use an external 220V regulator.

  - Turn on the power switch①,and the indicator will bright, and the screen will  display the time of the vibration.

  - Setting：

A：Setting the vibration time，press down the button⑦, the first LED on the left will bright on the  screen③,button⑧ have two function: the vibration will decrease when set the machine; and it the RESET button when the machine is stopping. After setting the vibration, press down the button⑦again, the second LED on the left will bright. Repeat the above steps，until the six LED on the left bright. After the six LED bighting about 8 seconds, Vibration time setting is completed, and the LED will be turn off.

B：Press down⑥RUN/STOP button, and the display screen③begin  Timing ，press ⑧ or ⑨buttons（VOLUME）to decrease or increase the vibration. The number will be display form 0 to 100 by adjustment. The machine will stop working when the setting time is over. If you want to test again, please press the RESET button⑧ for the next work.

ⅢAccessories

1．Use’s manual      1pcs

2．The fixed crews    4pcs

3．Rubber Rope      1pcs

MEIRUIKE INSTRUMENT

RK-3000 SERIES VIBRATION TESTER

OPERATION MANUAL

Shenzhen Meiruike Electronic Technology Co., Ltd

# Text boxes

1